## Slide 1
Smart Energy-Aware
Home Automation System
Wireless Appliance Control with Real-Time Current Monitoring and Overload Protection
ESP32 | 4-Channel Relay | ACS712 Current Sensor | I2C LCD

## Slide 2
Introduction
Home automation enables remote control and monitoring of electrical appliances, improving safety and energy efficiency.
This project presents a system that allows wireless control of up to four appliances using an ESP32, with a 4-channel relay module for switching, an ACS712 sensor for real-time current monitoring, and a 16x2 I2C LCD for status display.
An automatic overload detection mechanism switches off appliances when excessive current is detected.
Smart. Safe.
Energy-Efficient.
A complete IoT-based
appliance control solution

## Slide 3
Objectives
Design a wireless home automation system using ESP32 to control up to four appliances
Monitor real-time current consumption of connected loads using the ACS712 sensor
Display appliance status and current readings on a 16x2 I2C LCD
Implement automatic overload detection and protection
Improve overall household energy efficiency and safety

## Slide 4
Technology Used
ESP32 Development Board
Central controller & WiFi communication
4-Channel Relay Module
Switches appliances ON/OFF
ACS712 Current Sensor
Measures real-time load current
16x2 I2C LCD Display
Shows status & current readings
Jumper Wires & USB Cable
Connections and programming/power
Power Supply & Loads
Bulb / Fan / electrical appliances

## Slide 5
System Architecture
User
(WiFi)
ESP32
Controller
Relay
Module
Appliances
(Loads)
ACS712
Current Sensor
16x2 I2C LCD
(Status Display)
ESP32 reads current via ACS712, displays status on the LCD, and drives relays. If current exceeds the safe threshold, the relay is switched off automatically.

## Slide 6
Methodology
Hardware Setup & Sensing
1
ESP32 GPIO pins interfaced with the 4-channel relay module, each channel controlling one appliance
2
ACS712 current sensor connected in series with the load circuit to measure current drawn
3
Analog output of ACS712 read via ESP32 ADC and converted to current values using calibration
4
16x2 I2C LCD connected via SDA/SCL lines to display appliance status and current readings

## Slide 7
Methodology (continued)
Control Logic & Safety
5
ESP32 continuously monitors sensor readings; if current exceeds the safe threshold, the relay is switched OFF automatically
6
Users control appliances wirelessly via the ESP32's built-in WiFi for remote ON/OFF operation
7
Overall logic — relay control, current sensing, overload detection, and LCD updates — programmed using Arduino IDE
Overload protection turns OFF the load automatically — preventing equipment damage and electrical hazards.

## Slide 8
Output / Result
Wireless Control
ESP32 successfully controls up to four appliances via the 4-channel relay module, responding correctly to ON/OFF commands.
Real-Time Monitoring
ACS712 sensor accurately measures current consumption; readings and appliance status are shown live on the 16x2 I2C LCD.
Overload Protection
When current exceeds the set threshold, the corresponding relay is automatically switched OFF, confirming effective safety protection.

## Slide 9
Conclusion
The Smart Energy-Aware Home Automation System demonstrates a practical, cost-effective approach to modern home automation. Combining ESP32-based wireless control, real-time current monitoring with ACS712, and automatic overload protection enhances both convenience and safety.
The real-time display of appliance status and power consumption on the I2C LCD further improves user awareness of energy usage, laying a strong foundation for future enhancements such as mobile app integration, cloud-based monitoring, and predictive load management.
Future Scope
Mobile app integration
Cloud-based energy monitoring
ML-based predictive load management